TABLE OF CONTENTS

1. Introduction	3

2. End-uses included in the measurements campaigns	3

3. ID for end-use recordings and other measurements	3

4. Guidelines for preparation, Installation and Data handling	3

5. Description of measurement campaign in Belgium	3

6. Description of measurement campaign in Bulgaria	3

7. Description of measurement campaign in Czech Republic	3

8. Description of measurement campaign in Denmark	3

9. Description of measurement campaign in France	3

10. Description of measurement campaign in Germany	3

11. Description of measurement campaign in Greece	3

12. Description of measurement campaign in Hungary	3

13. Description of measurement campaign in Italy	3

14. Description of measurement campaign in Norway	3

15. Description of measurement campaign in Portugal	3

16. Description of measurement campaign in Romania	3

17. Equipment used for end-use measurement in the REMODECE project	3

# 1. Introduction

The overall objective of the REMODECE (Residential Monitoring to Decrease Energy Use and Carbon Emissions in Europe) project is to contribute to:

- Increased understanding of the energy consumption in the EU-27 households for the different types of equipment, the consumers’ behaviour and comfort levels.

- Identification of demand trends.

- Evaluation of the potential electricity savings in the residential sector that can implemented by existing means as very efficient appliances and reduced standby consumption.

The availability of high quality end-use data is an essential condition for the definition of policy recommendations to influence through a combination of increased energy efficiency of household appliances to be sold in the EU-27 in the next decade, as well as to influence the user behaviour in the selection and operation of that equipment. REMODECE collect data by new monitoring and surveying campaigns.

EU countries without earlier end-use load recording campaigns have as far as possible included all important end-uses as cooker, refrigerator, freezer, washing machine, tumble dryer, dishwasher, entertainment as TV, DVD and CD player, computer and peripherals, oil or gas burner including circulation pump, residential air condition and the 10 most used lamps as separate end-uses.

EU countries that already have executed end-use load recording campaigns (with data to be included in the EU database) have focused at appliances with a lot of changes: computer and peripherals, entertainment systems as home movie systems, game/playstation consoles, DVD players/recorders and Large plasma TV,  new Standby consumption by set-top box, DVD players/recorders and plasma TV, residential air conditioner and lighting (as many lamps as possible with first priority to CFLs and halogen lighting).

The campaign has included 100 homes with end-use recording in 2 weeks or one full month per home. Summer months with little use of lighting and customer absence due to holidays has as far as possible been avoided except for recording on air conditioners where the consumption in the summer months has to be recorded. In case of recording on appliances sensitive to temperature as air conditioner, the outdoor and indoor temperature has also been recorded.

The purpose of this D8 report is to give:

- The campaign concept of end-uses in focus with difference between “old” (contries that have already performed domestic end-use recordings) and “new” EU-countries.

- Developed ID system in order to handle all measurements with unique identify.

- The developed guidelines for preparation of measurements, installation, data retrieval, quality control and repair of data. This include standby measurement.

- Detailed description of the campaigns performed in each of the 12 countries with campaigns participating in Remodece.

- Description of equipment used in the end-use recording campaigns

# 2. End-uses included in the measurements campaigns

Due limited national budget for buying end-use recording equipment, priority lists on which end- uses to include was developed during the first months of the project.

Bulgaria, Czech Republic, Hungary and Romania (New countries)

- Total consumption (if it is not to difficult to establish)

- Washing machine

- Tumble dryer

- Entertainment as a group of appliances in living room: TV, DVD, CD, …

- Computer and peripherals as a group for home office

- Refrigerator (period consumption + spot metering of load at installation by SEM 10)

- Freezer (period consumption + spot metering of load at installation by SEM 10)

- 10 most used lamps individually or the sum of lighting by groups in the installation

- All kind of stand by consumptions recorded at the time of installation by SEM 10 including satellite amplifier, Internet connection, chargers, etc.

If possible add:

- sum of computer and TV set per teenager room

- cooker including oven

- dishwasher

- oil or gas burner including circulation pump

- Water heating

Belgium, Denmark, France, Germany, Greece, Italy, Norway and Portugal (Old countries)

  - Total consumption (if it is not to difficult to establish)

  - TV + VHS + DVD + Home Cinema

  - Large TV screen or other specialities might be recorded separately

  - CD + Stereo

  - Computer and peripherals as a group in office room

  - Sum of computer and TV set for every teenager room

  - 10 most used lamps individually or sum of lighting by groups in the installation

  - Air conditioning (only southern countries)

  - All kind of standby consumptions recorded at the time of installation by SEM 10, including satellite amplifier, setop boxes internet connection, chargers, etc.

If possible add:

    - Separate recording on individual appliances within the nine groups above

    - cooker including oven

    - washing machine, tumble dryer, dishwasher

Refrigerator and freezer consumption might be recorded over a short period along with spot metering of the load at time of installation by SEM10 equipment.



# 3. ID for end-use recordings and other measurements

It is necessary that all measurements and end-use load recordings from the participating countries have unique ID in order to perform data analysis in WP 5 (SINTEF responsible) and for storage in the EU database created in WP2 (Enertech responsible).

A ID system is developed and is composed by 15 digits including: cccc pp nnn aaaaaa

cccc is a country code

pp is the campaign number

nnn is the number of the household included in the program

tt aa nn is a number identifying each recording point/file that can be an appliance, the mains (total consumption per home) or a temperature

3.1.  Country code cccc

The code consist of the 1 followed by the national telephone code of the country, e.g. 45 for Denmark and 351 for Portugal.

1032 for Belgium

1045 for Denmark

1033 for France

1049 for Germany

1030 for Greece

1039 for Italy

1047 for Norway

1351 for Portugal

1359 for Bulgaria

1420 for Czech Republic

1036 for Hungary

1040 for Romania

3.2. Campaign number pp

The campaign number is a consecutive numbering of measurement campaigns.

In REMODECE we will use campaign numbers 01.

3.3. Household number nnn

The household number is the numbers of households participating in the campaign e.g. 1-100 for a campaign including 100 households.

3.4. Appliance number tt aa nn

- tt identify the type of appliance

- aa identify the specific appliance

- nn is the relative number of the appliance in case there is more than one.

Due to lack of recording equipment, the sum of consumption for several appliances may be  recorded summated by use of a multiple switch box (can be used for audiovisual, computer, lighting and small cooking appliances). In this case, aa must be a cluster code. Cluster recording should only be used when it makes sense to analyze the recorded data.

On/off recording of cluster lighting must in the data handling be split into data files for each lighting source in the cluster.

01  Cold appliances

01 01 01 Refrigerator 1

01 01 02 Refrigerator 2

01 01 03 Refrigerator 3

01 02 01 Fridge freezer 1

01 02 02 Fridge freezer 2

01 03 01 Chest freezer 1

01 04 01 Vertical freezer 1

01 05 01 American freezer 1

01 06 01 Vine fridge 1

02  Washing machines, dish washers...

02 01 01 Washing machine 1

02 02 01 Dish washer 1

02 03 01 Clothes dryer (without condenser) 1

02 04 01 Clothes dryer (with condenser) 1

02 05 01 Discharge clothes dryer 1

02 06 01 Washing machine with cloth dryer 1

02 07 01 Iron 1

02 08 01 Vacuum cleaner 1

02 09 01 Central hover 1

02 10 01 Steam cleaner 1

02 11 01 Sewing machine 1

03  TV

03 01 01 CRT TV <=55cm 1

03 01 02 CRT TV <=55cm 2

03 02 01 CRT TV >55 and <=72cm 1

03 03 01 CRT TV >72cm 1

03 04 01 LCD TV <=52cm 1

03 05 01 LCD TV >52 and <=81cm 1

03 06 01 LCD TV >81cm 1

03 07 01 Plasma TV <=107 1

03 08 01 Plasma TV >107 and <=120 cm 1

03 09 01 Plasma TV >120 cm 1

03 10 01 Video projector 1

03 11 01 LCD/Plasma TV controller 1

03 91 01 Cluster of TV + VCR 1

03 92 01 Cluster of TV + VCR/DVD 1

03 93 01 Cluster of TV + DVD 1

03 94 01 Cluster of TV + VCR + HI-FI 1

03 95 01 Cluster of TV + VCR/DVD + HI-FI 1

03 96 01 Cluster of TV + DVD + HI-FI 1

03 99 01 Cluster of other combination of TV and/or audiovisual appliances 1

04  Audiovisual appliances

04 01 01 Combined VCR/DVD 1

04 02 01 Combined VCR/TV 1

04 03 01 Combined HD/DVD 1

04 04 01 VCR 1

04 05 01 DVD player 1

04 06 01 DVD player and recorder 1

04 07 01 Home cinema 1

04 08 01 Games console 1

04 09 01 Hard Disc 1

04 10 01 Set top box with hard drive 1

04 11 01 Satellite/cable set top box 1

04 12 01 Digital terrestrial television box 1

04 13 01 Decoder 1

04 14 01 Satellite amplifier 1

04 15 01 Antenna booster 1

04 16 01 Audio/tuner amplifier 1

04 17 01 Subwoofer amplifier 1

04 18 01 Hi-Fi 1

04 19 01 Portable Hi Fi 1

04 20 01 CD player 1

04 21 01 Cassette player 1

04 22 01 Gramophone 1

04 23 01 Speakers 1

04 24 01 Security camera 1

04 25 01 Camera charger

04 26 01 Retro projector 100-150

04 27 01 Retro projector >=150

04 28 01 Active loud speakers 1

04 91 01 Cluster of appliances that accompany TV (amplifier, decoder, DVD) 1

04 92 01 Cluster of HI FI appliances (radio, CD, Gramophone etc.) 1

04 93 01 Cluster of home cinema and DVD 1

04 94 01 Cluster of home cinema, DVD and audio amplifier 1

04 95 01 Cluster of TV and HI FI appliances

04 99 01 Cluster of various TV and audiovisual appliances

05  Computer

05 00 01 Computer site 1

05 01 01 Desktop 1

05 02 01 CRT monitor <17” 1

05 03 01 CRT monitor 17” 1

05 04 01 CRT monitor >17” 1

05 05 01 LCD monitor <17” 1

05 06 01 LCD monitor 17” 1

05 07 01 LCD monitor >17” 1

05 08 01 Desktop + CRT monitor <17” 1

05 09 01 Desktop + CRT monitor 17” 1

05 10 01 Desktop + CRT monitor >17” 1

05 11 01 Desktop + LCD monitor <17” 1

05 12 01 Desktop + LCD monitor 17” 1

05 13 01 Desktop + LCD monitor >17” 1

05 14 01 Desktop + monitor + UPS 1

05 15 01 Laptop 1

05 16 01 Laptop  + CRT monitor <17” 1

05 17 01 Laptop  + CRT monitor 17” 1

05 18 01 Laptop  + CRT monitor >17” 1

05 19 01 Laptop  + LCD monitor <17” 1

05 20 01 Laptop  + LCD monitor 17” 1

05 21 01 Laptop  + LCD monitor >17” 1

05 91 01 Cluster of desktop + CRT monitor + printer 1

05 92 01 Cluster of desktop + CRT monitor + printer-scanner-copier 1

05 93 01 Cluster of desktop + LCD monitor + printer 1

05 94 01 Cluster of desktop + LCD monitor + printer-scanner-copier 1

05 95 01 Cluster of desktop + CRT monitor + printer + TV + HI-FI 1

05 96 01 Cluster of desktop + LCD monitor + printer + TV + HI-FI 1

05 97 01 Cluster of laptop + printer 1

05 98 01 Cluster of laptop + printer + TV + HI-FI 1

05 99 01 Cluster of PC and/or peripheral computer appliances 1

06  Peripheral Computer appliances

06 01 01 Inkjet printer 1

06 02 01 Laser printer 1

06 03 01 Photo printer 1

06 04 01 Printer-scanner-copier 1

06 05 01 Scanner 1

06 06 01 Copier 1

06 07 01 Modem 1

06 08 01 Internet/TV/Phone box 1

06 09 01 Router 1

06 10 01 WIFI module 1

06 11 01 Wireless mouse 1

06 12 01 Wireless headset 1

06 13 01 Computer amplifier 1

06 14 01 External hard disk 1

06 15 01 Electrical CD storage 1

06 16 01 USB hub 1

06 17 01 Fax 1

06 18 01 Paper shredder 1

06 19 01 Picture receiver 1

06 20 01 Picture transmitter 1

06 99 01 Cluster of various peripheral computer appliances

07  Air conditioning + heating

07 01 01 Mono split 1

07 02 01 Multi split 1

07 03 01 Heat pump air/air 1

07 04 01 Heat pump air/water 1

07 05 01 Heat pump water/air 1

07 06 01 Heat pump water/water 1

07 07 01 Circulation pump 1

07 08 01 Humidifier 1

07 09 01 Mobile air conditioner 1

07 10 01 Fan 1

07 11 01 Well pump 1

07 12 01 Gas burner for heating 1

07 13 01 Oil burner for heating 1

07 14 01 Electric water heater 1

08-12 Lighting ID (see below)

tt identify the type of lighting source. In case of cluster recording on more than one lighting source, use code 99.

aa identify the room using the following codes:

00 Total lighting consumption

01 Bar

02 Bathroom

03 Bedroom for parents or guests

04 Corridor

05 Dining room

06 Entrance

07 Garage

08 Guest room

09 Hall

10 Kitchen

11 Living room

12 Office

13 Outside

14 Sauna

15 Stairs

16 Store room

17 Studio

18 Washing room

19 Cellar

20 Bedroom for children

21 Security lighting

nn identify the relative number of the single lamp. In case of three bedrooms with a total of 4 incandescent lamps, the numbers will be 01-04

In case there is more than one room of one type, you can use the first digit in nn to specify the room number and the last digit to identify the relative number of the single lamp. Example: 08 20 11 (tt aa nn) is the first incandescent lamp in no 1 bedroom for children, while 08 20 21 is the first incandescent lamp in no 2 bedroom for children.

Using this system there can maximum be 10 lamps of the same type in a room but that should normally not be a problem.

08  Lighting Incandescent

Examples 08 02 01 Incandescent no 1 in bathroom

08 02 02 Incandescent no 2 in bathroom

08 03 01 Incandescent no 1 in parents bedroom

08 20 01 Incandescent no 1 in bedroom for children

99 03 01 Cluster no 1 in parents bedroom (e.g. including 2 incandescent + 1 halogen)

09  Lighting Low voltage (12 V) halogen

10  Lighting 230 V halogen

11  Lighting Flourescent tubes

12  Lighting CFL

14 LED

13 Cooking

13 00 01 Cooker 1

13 01 01 Oven 1

13 02 01 Microwave oven 1

13 03 01 Bread maker 1

13 04 01 Espresso coffee machine 1

13 05 01 Coffee machine 1

13 06 01 Ice cube maker 1

13 07 01 Kettle 1

13 08 01 Toaster 1

13 09 01 Food processor 1

13 10 01 Juice blender 1

13 11 01 Cooker hood 1

13 12 01 Egg cooker 1

13 99 01 Cluster of cooking appliances (except cooker) 1

15 Reserve

16  Other appliances

16 00 01 Electrical seat 1

16 01 01 Electrical bed 1

16 02 01 Automatic door 1

16 03 01 Water softener 1

16 04 01 Aquarium 1

16 05 01 Whirlpool spa bath 1

16 06 01 Sauna 1

16 07 01 Hair dryer 1

16 08 01 Electric toothbrush 1

16 09 01 Alarm system 1

16 10 01 Gas sensor 1

16 11 01 Guitar amplifier 1

16 12 01 Turntable table 1

16 13 01 Electric clock 1

16 14 01 Electric clock with radio 1

16 15 01 Electric clock with radio and CD 1

16 16 01 Battery charger 1

16 17 01 Water bed 1

16 18 01 Curling iron 1

16 19 01 Iron for steam dry ironing 1

16 21 01 Phone call identifier 1

16 22 01 Simple answering machine 1

16 23 01 Phone-fax 1

16 24 01 Mobile phone charger 1

16 25 01 Cordless phone 1

16 99 01 Cluster of several small other appliances	1

17  Total consumption (mains)

17 00 01 Total consumption of the site.

17 01 01 Total consumption for installation zone/group 1 (recording on a zone/group in the installation)

17 01 02 Total consumption for installation zone/group 2

17 01 03 Total consumption for installation zone/group 3

17 02 01 Total consumption residual (mains subtracted all end-use recordings)

18  Temperatures

18 01 01 Outside temperature

18 02 01 Air conditioned room 1, mention the type of room

18 02 02 Air conditioned room 2, mention the type of room

18 02 03 Air conditioned room 3, mention the type of room

18 03 01 Electric heated room 1, mention the type of room

18 04 01 Room 1 without air con. or elec. heating, mention the type of room

# 4. Guidelines for preparation, Installation and Data handling

4.1 Preparation

( Make appointment with the residents for the next month in order to avoid delays

( Confirm appointments

( Prepare your recording equipment (programming and configuration)

( Prepare more equipment than you need to avoid not having enough

( Site list for households including address, phone numbers and roadmap.

4.2 Installation

( Equipment for momentary power monitoring e.g. SEM10.

( All type of recording equipment

( At least one extension cord with multiple plugs

( ID appliance code list

( Installation sheet including appliances and standby consumption measured

( Questionnaire to be filled on site

( Check the switch box (size, age, quality and safety) for if it is possible to install.

( Start by explaining to the residents the way the measurement campaign will be conducted and the type of equipment you will install in their household. If the residents are negative then cancel the participation and find another household which is better than later experience some of the equipment are disconnected.

( Never give tips on how to reduce the electricity consumption before the end of the monitoring campaign.

( Never monitor two or more appliances with the same equipment unit before you know from the manufacturer if it is possible (except for the audio and computer equipment).

( Take photos from the switch box before and after the recording equipment is installed in order to avoid discussions later of the changes carried out.

( Using the SEM10, take care always to unplug the appliance from the SEM10 before unplugging the SEM10 from the main power.

4.3 Useful things to bring with you at installation

( multiplug (20)

( dominos

( male and female plugs

( wire     ( 1,5 mm2	  ( 2,5 mm2	( 4 mm2    ( 6 mm2

( cable    (  2x1,5 mm2   ( 2x2,5 mm2   ( 3x1,5 mm2   ( 3x2,5 mm2

( adapters 20/16 A

( Colson ring clamps

( Nails, fixture accessories.

( Pocket lamp

( tools: screw drivers (8), nippers, stripper, phase tester, cutter, hammer, dry rag

( Tape

( Voltmeter

( writing support material

( scrap paper

( thumbtack

( Cork

( A little mirror for reading appliance information at their back

4.4 Information to collect at the time of installation

At the time of installation of end-use recording we must use the opportunity to collect more information by:

  - Collecting information about every end-use to be recorded - this is especially important when several appliances go in as a sum and one end-use recording.

  - Note of consumption information e.g. from appliance label

  - Size of the family, type of home and area

  - Spot metering on small appliances not included in the end-use recording – standby consumption is very important to measure e.g. by SparoMeter (equipment description later in the report).

The table below includes a list of appliances with standby consumption and serve decisions in every country on which instantaneous standby consumptions to include in the measurements.

The following system was decided for inclusion of standby consumption in the WP2 database:

- Deliver data in a text files or an excel file including four columns: household number, appliance ID tt aa nn (see the description in section 3), the measured standby power (in W) and extra appliance description/comment.

- Example for household number 9:	9, 030201, 3500, Sony LCD TV 60 cm

9, 061301, 2200, Motorola ADSL modem

9, 160103, 1850, Mini oven BcB2

...

| Type | Appliance | Type | Appliance |
| --- | --- | --- | --- |
| Cold | Refrigerator | TV/Video | CRT TV |
|  | Refrigerator - freezer |  | LCD TV |
|  | Chest freezer |  | Plasma TV |
|  | American freezer |  | Videoprojector |
| Cooking | Coffee machine |  | DVD player |
|  | Cooker (oven + hotplate) |  | DVD recorder |
|  | Microwave oven |  | Hard Disc |
|  | Kitchen oven |  | VCR |
| HiFi | HiFi system |  | Combined VCR/DVD |
|  | Speakers |  | Combined VCR/TV |
|  | CD player |  | Combined HD/DVD |
|  | Clock-radio |  | Home cinema |
| Office | Desktop |  | Satellite/cable set top box |
|  | CRT monitor |  | Digital terrestrial television box |
|  | LCD monitor |  | Games console |
|  | Laptop |  | Security camera |
|  | Ink-jet printer | Various | Air conditioning system |
|  | Laser printer |  | Alarm systems |
|  | Photo printer |  | Vacuum cleaner |
|  | Printer-scanner-copier |  | Security lighting |
|  | Scanner |  | Toothbrush |
|  | Modem |  | Gas sensor |
|  | Internet/TV/Phone box |  | Battery charger |
|  | Computer amplifier |  | Halogen lamp |
|  | External hard disk |  | Clothes-washer |
|  | Electrical CD storage |  | Dishwasher |
|  | WiFi module |  | Electrical bed |
|  | Wireless mouse |  | Electrical seat |
|  | Router |  | Alarm clock |
| Telephony | Phone call identifier |  | Hairdryer |
|  | Simple answering machine |  | Condensation clothes-dryer |
|  | Phone-fax |  | Discharge clothes-dryer |
|  | Mobile phone charger |  | Water treatment |
|  | Cordless phone |  |

4.5 Data handling

All partners need to set up careful systematic procedures for handling of all recorded load research data including the following functions:

- Handling the all customers and load appliances by systematic ID (see part 3).

- Installation with training and documentation for routines.

- Remote reading of data every night with daily control of data. Remote reading is preferable due to the high control, but alternatively data can be taken by visit of the customer every week or at least every month.

- Quality control.

- Data repair/correction of failures.

- Storage of accepted data in national database.

- Load Research analysis facilities for own analysis.

4.5.1 ID of every recording point

See part 3 concerning the ID system to use.  Enertech has provided installation sheets which can be used to keep track on all information at installation including standby consumptions measured.

4.5.2 Remote reading, integration period and type of recording

Remote reading is a benefit since data can be taken home every night and data is thus maximum lost for a day in case the equipment fails – this is especially a benefit for long campaigns while campaigns with recording only a month per customer maximum risk a loss of one month data. In case of no remote reading, it is convenient if the equipment have internal storage for the campaign period.

End-use recording in other EU project are nearly all done with 10 minutes integration period while some countries e.g. the Nordic countries has a tradition of using equipment with 15 minutes integration period. It is recommended to use 10 minutes integration period in Remodece as far as possible.

Also the total load from the electronic meter has to be recorded with 10 minutes integration period which makes it possible to calculate the residual of small appliances as the difference between the total load and all the end-uses recorded.

End-use recording is most easily installed by the plug in type which is also giving less visual discomfort for the people living in the houses and much smaller costs for installation. Clamps or cable junction must be used if the appliances can not be plug in.

4.5.3 Quality Control of data

Data must go through a standardized quality control including functions for correction/repair of data in the process or later.

No data must pass into the load research database before the user of the system has approved data.

Types of control to perform:

- Control of start of new file fits with stop of last file

- Control for excessive zero intervals

- Data values should be within a set of high/low boarders specified by the user.

- Load factor should be within a set high/low boarders specified by the user.

- Graphic display of data

4.5.4 Data Repair and Correction:

There shall be facilities for manual editing of data which the option of correcting, adding or deleting data or intervals of data. Manuel editing shall include graphical display of data. Small holes in data may be repaired based on load on same types of days and energy consumption for the period.

Any repair/correction of metered data shall be traceable by

- List of files with problems

- List of missing data for at given period

- List of data which is not accepted due to bad quality

4.5.5 National database

Accepted data is to be stores in a load recording database using the systematic ID of each customer and appliance.

There shall be procedures for data backup as well as the possibility to restore the original data.

# 5. Description of measurement campaign in Belgium

Every country describe their measurement campaign including:

- Description of the domestic customer segment included in the campaign

- Measurement period

- Recording period per home

- Is total consumption per home included in the recording?

- End-uses recorded

- Special recording e.g. air condition, electric heating, temperature, ...

- Problems meet in the measurement campaign

- Own analysis results (besides the cross country analysis SINTEF Energy performs in the project)

# 6. Description of measurement campaign in Bulgaria

# 7. Description of measurement campaign in Czech Republic

# 8. Description of measurement campaign in Denmark

# 9. Description of measurement campaign in France

# 10. Description of measurement campaign in Germany

# 11. Description of measurement campaign in Greece

# 12. Description of measurement campaign in Hungary

# 13. Description of measurement campaign in Italy

# 14. Description of measurement campaign in Norway

# 15. Description of measurement campaign in Portugal

# 16. Description of measurement campaign in Romania

# 17. Equipment used for end-use measurement in the REMODECE project

17.1a SEM 10 – Stand by Energy Monitor

Website: http://www.nzr.de

Features:

Manual reading of:

- Energy consumption in kWh (pr. Day, week or 30 days);

- Energy costs, currency-independent display (costs);

- Minimal power (W);

- Maximal power (W);

- Current power (W);

- Current current-consumption (A);

- Current voltage (V).

Experience with use of the equipment:

- ISR, University of Coimbra, Portugal

Price/unit: 40 €

17.1b SparoMeter NZR 230

Website: http://www.sl-electric.dk/

Features: Same equipment as SEM 10

Experience with use of the equipment:

- Most of the participants  e.g.  CEU University, Hungary

Price/unit: Depend on the number of units bought.

17.2 Power Detective

Website: http://www.sl-electric.dk/

Features:

- Load recording including 70000 loads each with time stamp

- Integration period 1, 5, 10 , 15, 30 or 60 minutes

- Able to record loads in the interval 0,2 – 3600 W (max 2% failure)

- Configuration by power line or internet (through router) connection

- Display of kWh, costs, minimum and maximum load plus actual load, current and voltage

- Data are transferred to a data collector unit by m-bus protocol

- Remote reading by Internet router by TCP/IP 10/100 base T(TX) protocol

- Optional can be added a relay for demand response (load management)

Experience with use of the equipment:

- SINTEF Energy in Norway and Danish utilities

Price/unit:

- 116 € per Power Detective unit (depend on the number you are buying).

- 773 € for Web-server with memory card to collect all the data by power line from all power detective units sued in the house.

- 57 € for powerline modem with USB interface.

17.3 CE Leistungs-energiemessgerate

Website: http://www.christ-elektronik.de/www/produkte/messgeraete/leistungs-energiemessgeraete/

Features:

- Version 1 display W and kWh

- Version 2 display W, kWh, V, A and kWh/hour (average?) and costs

- Version 3 also has a pulse output to record load time series and can also measure reactive load.

- Christ also sell a meter recording W and kWh and optional pulse output for load recording.

Experience with use of the equipment:

- E-ster bvba, Belgium (has 77 CE version 1 and 3 CE version 3)

Price/unit: 	120-150 € for version 1 of the equipment depending for 10-10 pieces

Around 220 € for version 3 and around 150 € for software

17.4 EMU 1, EMU 10.MEMO Electronic Meter

Web-site: http://www.emuag.ch/englisch/produkte/steckdosen/steckzaehler.htm

Features:

The electronic meter EMU 1 provides instantaneous values.

EMU1.x4K and EMU-CHECK plug-in energy and power analyser with consumption cost accumulation in EURO by setting cost per kWh.

EMU 10. MEMO is used to find the quality and quantity of the electricity  1 consumption as momentary values or load profiles. It is a single-phase electronic electricity meter of class 2 accuracy having a maximum current rating of 16 A. It measures and stores the following values:

– Real Voltage (momentary value)  176 – 264 V

– Real Current (momentary value)  0.010 – 16 A

– Active Energy 0.00 – 999 kWh

– Apparent Energy 0.00 – 999 kVAh

– Reactive Energy 0.00 – 999 kvarh

– Active Power (momentary value)  0.000 – 4.22 kW

– Active Power Demand 0.00 – 4.22 kW every 5, 10, 15, 30 or 60 minute

– Apparente Power (momentary value) 0.000 – 4.22 kVA

– Reactive Power (momentary value)  0.000 – 4.22 kvar

– Power Factor (momentary value)  c 0.02 – 1.00

– Network Frequency (momentary value)  F 45.0 – 65.0 Hz

The EMU 10. MEMO metering system is an open system including:

- Electronic Meter EMU 10. MEMO with power plug or clamp-on type current transformer

- Bi-directional infra-red Interface for data transfer and configuration

- Battery-supported real time clock.

- Synchronisation of values in several units by programming the date and hour of the start along  with the time interval between the reading of values (between 6 seconds and 99 days)

- NVRAM (non-volatile data storage memory) capacity is 256 kbytes (optional 128 or 512 kB) that can include 7 electrical values with time stamp measured every minute for up to 7 days.

- The display of values might be faded out on the instrument by configuration.

- Configuration and data transfer Software EMUMEMW

Experience with use of the equipment:

- ISR, University of Coimbra, Portugal

- ADEME, France

Price/unit (€): 							      1-9 units	  10-24 units

EMU 10. MEMO “Starter set” (1 unit, optical interface and EMUMEMW) 		592.1

Additional EMU 10. Memo (in case software is used at the same pc)		526.3	   	526.3

EMU1.x4K									138.2		134.9

EMU1.x8K or EMU1.x9K 							197.4		193.4

EMU-Check ”Cost” or EMU-Check ”Power Level”				  71.1		  69.1

17.5 Enertech Data Loggers

1.         2.

3.

Website: http://siedler.club.fr

Products and features:

- Serial watt data logger for maximum 2600 W that works autonomous for 1,2 year with 10 min. integration period. Data are then transferred to pc by Oscar software.

- Lamp meter logger that require no connection to supply network. Recording up to 32000 events time of the events of turning lighting on and off. Oscar software transfer data to pc.

- Wattmeter with amp clamp and pulsemeter (the weight of one pulse is 0.5 Wh). It works autonomous for 1.2 year with 10 min. integration period and measurement range 3W – 22kW. Data are then transferred to pc by Oscar software.

- Thermometer (-50 – 120OC) 1,2 year data with 10 min. integration period. Oscar software.

Experience with use of the equipment:

- Many of the participating countries are using this system or the former system manufactures by Enertech.

Price/unit:  Product 1: 120 €,  2: 35 €,  3: 165 €,  4: 45 €  and Oscar software: 500 €.

17.6 INNOVUS MyHome@

1-phase plug-in 	   	    3-phase   	       1-phase Lighting

Central gateway	    Remote control      Wall mount control

S0 pulse ReaderCom for energymeters

Website: 		www.Innovus.dk

Features:

- Home automation system using wireless communication by the Z-wave system

- Management, controlling and data access by interfaces pc, local touch screen, tv screen plus set top box or Mediacenter, cellular phones or PDA.

- 1-phase plug-in unit for load recording but can also serve as relay based switch (on/off).

- 3-phase cable junction for load recording but can also serve a relay based switch (on/off).

- Lighting unit cable junction for load recording but can dim the lighting by touching the unit or by remote control or software based front end.

- Central gateway coordinating all data flow and storing of data for several months.

- MyHome@ application for user management also include consumption feedback.

- Control by Web-interface, own or B&O remote control unit or wall mount switch.

- S0 pulse ReaderCom for recording on energy meters.

Price/unit (approx. dimensions l/w/h [mm]):

- MyHome@ softwareapplication  	€ 8 product fee + €1 monthly license fee

- 1-phase plugin unit (120 x 65 x 40) 			  50 €

- 3-phase unit						107 €

- 1-phase lighting unit (diameter 90, height 30) 	  47 €

- Central gateway (120 x 120 x 40) 			162 €

- Remote control unit (180 x 30 x 25 ) 		  47 €

- Wall mount controller ( 65 x 65 x 15) 		  36 €

- S0 pulse ReaderCom for energymeters		  57 €

This equipment used by: Denmark

# Text boxes

Project no.: EIE/05/124/SI2.419657

Project acronym: REMODECE

Full title of the action: Residential Monitoring to Decrease Energy Use

and Carbon Emissions in Europe

PRELIMINARY DRAFT

Report D8

MEASUREMENT CAMPAIGNS

End Use Recording in the Residential Sector

Casper Kofod

Energy piano

28-07-2007